## Slide 1: Prosthetics and Motor Function: Implications for Coordination and Brain Activity
James Pierce
June 8, 2018
Advisor: Jorge M. Zuniga, Ph.D.

## Slide 2: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 3: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 4: Introduction
The Centers for Disease Control and Prevention (CDC) estimate that about 1,500 babies are born with upper limb deficiencies (ULDs) every year
Most children with ULDs experience partial limb loss congenitally through Amniotic Band Syndrome (ABS)
  Characterized by in utero digit or limb loss
  Caused by the infiltration of fibrous connective tissue bands from the amnion into the uterus
ABS most commonly leads to amputation of the left upper limb, but can also affect other limbs
  20% of children with in utero amputation have bilateral, trimembral or quadrimembral reductions
  CDC cites developmental and quality of life (QoL) problems related to ULDs
Krebs D, Edelstein J, Thornby M. Prosthetic management of children with limb deficiencies. Physical Therapy. 1991;71(12):920.

## Slide 5: Introduction
It has been proposed that ULDs can lead to QoL detriments such as:
  Delayed or absent developmental milestones
  Mobility and self-care limitations
  Deficits in social acceptance
Only 1 in 9,400 of children with ULDs are considered for prosthetic fitting due to:
  Rapid growth
  High prosthesis cost
  Lack of insurance coverage
  Inadequate device functionality
  Of those that receive a prosthesis, there is also a high rate of device abandonment

## Slide 6: Introduction
Early age fitting and prosthesis use have been suggested to aid motor development and function
  Prevalence of ULDs is too low to create high power studies determining the true value of early prosthesis fitting
Prosthesis simulators could be one option to improve the design/functionality and prescription of devices despite the small population of pediatric amputees
  Much larger pool of research subjects can be made available
  Amateur prosthesis conditions can be tested more easily

## Slide 7: Introduction
Additive manufacturing technologies have the potential to produce prostheses that are:
  More useful
  Low-cost
  Customizable
  Quickly produced
There exists a need to evaluate prosthesis usage in a more quantifiable terms
  Brain activity in the motor cortex of ULD children is unexplored
  Bimanual coordination effects of prostheses are currently unknown
The quantification of these measures could provide valuable information regarding the motor control of children with ULDs
  Findings could aid in the improvement of the current prosthetic rehabilitation paradigm
http://enablingthefuture.org/wp-content/uploads/2014/02/shea2.jpg

## Slide 8: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 9: Purpose
To determine the influence of upper-limb prostheses and prosthetic simulators (compared to typically developing control children) on:
Brain activity in the motor cortex
Bimanual coordination

## Slide 10: Aims/Hypotheses
Specific Aim 1: Determine differences in coordination and dexterity among upper-limb prosthesis, prosthetic simulator, and typically developing control groups during performance of a bimanual coordination task.
  Hypothesis 1a: Bimanual coordination will be significantly higher in the control group than prosthesis and simulator groups.
  Hypothesis 1b: Gross manual dexterity will be significantly higher in the control group than prosthesis and simulator groups.
Specific Aim 2: Identify the influence of upper-limb prostheses and prosthetic simulators on brain activity in the motor cortex during the performance of different motor tasks compared to typically developing control children.
  Hypothesis 2a: Brain Activity in the motor cortex will be significantly increased, possibly due to exploratory movements, for both prosthetic and simulator conditions compared to the control group.
  Hypothesis 2b: Brain Activity in the motor cortex will be less lateralized for both prosthetic and simulator conditions compared to the control group.
Specific Aim 3: Determine differences in perception (embodiment and agency) of the body among upper-limb prosthesis, prosthetic simulator, and TD control groups.
  Hypothesis 3: Embodiment and agency of the non-preferred arm will be significantly higher in the control group compared to prosthesis users.

## Slide 11: Significance
The neurological and motor control mechanisms that could explain the high prosthesis rejection rate observed in children with ULDs have not been properly examined
This information is critical to enhance our limited knowledge of how children increase the number of available motor repertoires through selection
This information would be helpful to develop rehabilitation programs aimed to:
  Reduce prosthesis rejection/abandonment
  Increase the functional use of the prosthesis

## Slide 12: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 13: Theoretical Framework
Neuronal Group Selection Theory (NGST):
  The brain is dynamically organized into neuronal networks or neuronal groups
    Structure/function of these networks is influenced by development and behavior
  Proposes that motor development is characterized by two phases of variation:
    Primary Variability (0-1 year of age) – Motor activity is variable, exploratory, and not based on environmental conditions
    Secondary Variability (> 1 year of age) – Child learns to select the most efficient motor strategy for a specific scenario based on active practice from a “variable movement repertoire”
      Secondary variability of all motor functions does not obtain its adult configuration until adolescence

## Slide 14: Theoretical Framework
Neuronal Group Selection Theory (NGST):
  ULD children may lack a developed representation of the affected limb in the motor cortex
  This underdeveloped representation likely leads to deficits in the motor repertoire for activities involving the affected limb
  Prosthesis usage has been proposed as a surrogate for the missing partial limb
    Has the potential to enlarge the primary neuronal networks related to the affected limb
    Could lead to a richer motor repertoire
http://www.deictic.net/wp-content/uploads/2013/08/universe_7_2.png

## Slide 15: Theoretical Framework
Body Schema and Body Image:
  Body schema – A central, action-related representation of spatial characteristics of the body, which includes:
    Length of body segments
    Hierarchical structure
    Form of body surfaces
  Body image – The conscious visual representation of how we see our bodies from outside
    Not closely related to motion control
    The awareness an individual has of their body’s form
    Individuals focus disproportionately more on specific body areas than on others
ULDs influence on body schema/image:
  Residual limb is perceived to be smaller and shorter
    Telescopes to more accurate length with prosthesis usage
  Phantom limbs may be present
    Much less common in congenital amputations than traumatic amputations
  Prosthesis use has been shown to improve the mental representations of the affected limb over time

## Slide 16: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 17: Summary of Review of Literature
Quality of Life:
  Qualitative measurement tools indicate limited usefulness of prostheses as rehabilitative tools
    Functionality is only significantly improved for specialized activities
  Quantitative measures show potential improvements overlooked by qualitative measures
    Improvements in dexterity, tactile sensation, coordinated motions of the hand, and proprioceptive feedback have been observed
Neural Representation of the Missing Limb:
  Differences exist in brain regions responsible for residual limb control/proprioception
    Only 20% of congenital amputees experience phantom limb sensation
    Experimental activation of associated brain areas fails to elicit sensations in missing limbs
  These differences may indicate modified neuronal group selection and body schema in ULD children
    Neuronal groups are developed through somatosensory input, which is missing in ULDs
    Similar modified neuronal group selection has been observed in cerebral palsy (CP) and developmental coordination disorder (DCD)

## Slide 18: Summary of Review of Literature
Coordination:
  Somatosensory deficits lead to differences in interlimb coordination
    Spinal cord injury and deafferentation negatively impact coordinated and cognitively demanding motions
  Handedness can cause temporal coordination deficiencies in cognitively demanding tasks
Viability of Prosthetic Simulators:
  Simulators have been shown to produce similar learning effects to novice amputees
  These devices can improve the power of studies performed with prostheses

## Slide 19: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 20: Methodology: Participants
Two groups of children
  Unilateral upper-limb deficiencies (ULD, n = 5)
  Typically developing (TD, n = 5) group using a prosthesis simulator (TD-Simulator)
  Typically developing control children (TD-Control)
Inclusion Criteria:
  Aged 3-16 years with unilateral upper-limb congenital reductions of any digit, hand, arm, or shoulder
  Any subjects with prior prosthesis experience must cease usage for at least six months prior to the study
Exclusion Criteria:
  Participants with upper extremity injury within past month
  Medical conditions that are contraindications for wearing a prosthesis
    Skin abrasions
    Musculoskeletal injuries of the upper limbs
All groups were age- and sex-matched to the ULD population
  Simulator users were also matched to amputation level
Demographics |  |  | 
 | N | Age (Years) | Amputation Level
TD | 5 | 8.60 ± 2.79 | -
ULD | 5 | 8.80 ± 3.11 | 2 Transradial 3 Partial Hand
TD = Typically Developing; ULD = Upper Limb Deficient |  |  | 

## Slide 21: Methodology: Recruitment
Recruitment Methods:
  Referrals from industry and healthcare collaborators (ULD subjects)
  Employee announcements at university campuses
  Word of mouth
  Mail invitations
Subjects were admitted to the study following informed assents or parental written consent as approved by the Institutional Review Board.
  Children under 6 years of age required a parental permission form
  Children age 6 to 18 were given an assent signed by the children and their parents

## Slide 22: Methodology: Apparatus/Materials
3D Printer Specifications:
  Prosthetic devices were manufactured on desktop and industrial 3D printers (Ultimaker 2+ Extended, Ultimaker B.V., Geldermalsen, The Netherlands and Uprint SE Plus by Stratasys, Minnesota, USA)
  Prostheses were produced from polylactic acid (PLA) and acrylonitrile butadiene styrene (ABS)
https://www.3dhubs.com/s3fs-public/uPrint_1.jpg
https://maker13.com/wp-content/uploads/2017/04/Ultimaker-2-Extended-2.jpg

## Slide 23: Methodology: Apparatus/Materials
Prosthetic Device/Simulator:
  Body-powered, manually adjustable and produced primarily using 3D printers
  Aids in the performance of bimanual and unilateral activities with a functional grasp
  Index finger and thumb are oriented in opposition to facilitate cylindrical grasp and tip pinch
  Silicone finger pads are added to provide enhanced traction and pliability
  Voluntary-Close (VC) in grip style
    Operated through the actuation of a cable attached to the ventral sides of the phalanges
  Custom scaled and fitted to a specialized socket
Parts were printed at 35%-40% infill density (hexagon pattern for desktop, crosshatch for industrial)
0.15-.25 mm layer height and 0.8mm shell thickness

## Slide 24: Methodology
Dependent Variables:
  Gross manual dexterity
  Temporal interlimb coordination
  Embodiment and body image
  Hemispheric dominance
  Brain activation patterns
Independent Variables:
  Prosthesis conditions
    No prosthesis (TD-Control)
    Prosthesis simulator (TD-Simulator)
    ULD Prosthesis (ULD)

## Slide 25: Methodology: Gross Manual Dexterity
“Box and Block” test as a measure of unilateral upper limb gross dexterity
  Small, partitioned box filled with identical blocks
  Number of blocks transferred between partitioned areas of the box is used as a measure of motor function
    Must be transferred individually to assess dexterity
  Testing takes place over 1 minute, and is repeated to ensure reliability of results
  Task was performed for both preferred and non-preferred hands
Do EY, Hsiao C, Zhao C. The digital box and block test automating traditional post-stroke rehabilitation assessment. PerCom Workshop. 2013.

## Slide 26: Methodology: Bimanual Coordination
Instrumented reaching tray to assess temporal coordination during reaching tasks
  Relative timing for each component of task motion was recorded for both unimanual and bimanual conditions
  Quantifies relative phase differences between prosthesis users, simulator users and typically developing controls
  Interlimb coordination can be quantified through timing differences in sensor triggering
    Closer timing corresponds with better interlimb coordination
    Positive asynchrony values indicate leading task motion with preferred hand
Kilbreath SL, Crosbie J, Canning CG, Lee MJ. Inter-limb coordination in bimanual reach-to-grasp following stroke. Disability and Rehabilitation. 2009:1435.

## Slide 27: Methodology: Body Schema Incorporation
Embodied Sense of Self Scale (ESSS) – Assesses the experiences of the aspects of sense of self
  Three subscales:
    Ownership – “This limb belongs to me”
      How an item is subjectively incorporated into one’s body representation
      An item is considered to be embodied when incorporated into human body representation and recognized as one’s own body parts
    Agency – “I am in control of this limb”
      Stems from congruence between a motor prediction and its predicted sensory feedback
    Narrative – How the self extends over time
      Includes identity, autobiographical memory, and intentions for the future
Body Focus Questionnaire (BFQ) – Used to gauge the relative weighting of focus on different parts of the body
  Participants choose the limb they are able to envision more clearly from a pair of limbs
  Nine scales of awareness for various body parts
    Arms, Front/Back Side, Right/Left Side, Head, Eyes, Mouth, Stomach, Legs and Heart

## Slide 28: Methodology: Hemispheric Dominance
Laterality Index (LI):
  LI measures which hemisphere experienced a larger change in HBO during task performance
    Normalizes activation differences between channels
    Negative values indicate left hemisphere dominant activation
    Positive values indicate a right hemisphere dominant activation
  Uses filtered HBO data taken from functional near-infrared spectroscopy (fNIRS) task analysis
    Box and Block: 60 seconds of task data

## Slide 29: Methodology
Procedure:
3D Scanning of residual limb, anthropometric measurements, reference photographs
Design/Scaling of Prosthesis, manufacturing of the device, ensuring fit on subject
Functional Testing
Gross manual dexterity Functional Assessments Qualitative Assessments
Bimanual Coordination Brain Activation/Hemodynamics Hemispheric Dominance
Initial Fitting

## Slide 30: Methodology: Design
Subjects were first fitted with a continuous wave 24-channel fNIRS system (Hitachi ETG-4000, Hitachi Medical Corporation, Tokyo, Japan)
  Sampling frequency of 10 Hz
  Two different wavelengths will be used (695and 830 nm)
  Probe set will use 10 sources and 8 detectors (3 cm spacing)
  Adjustable headgear will be positioned on the head following 10–20 international system
    Center of the headgear is aligned with the vertex (Cz)
    Lateral channels cover the area around C3 and C4 landmarks
  0.02 Hz high-pass filter and 0.5Hz low-pass filter
    Removes slowly drifting signal components

## Slide 31: Methodology: Design
Box and Block task was then performed for both dominant and non-dominant hands
  Three times per hand
  30 seconds of rest between trials
    Allows fNIRS readings to return to resting baseline
Subjects then performed the bimanual coordination tasks
  Three task conditions:
    Unimanual reaching with each hand
    Simultaneous bimanual reaching
  Performed three times per condition
  30 second rest period between trials
Each subject visit lasted roughly one hour
Kilbreath SL, Crosbie J, Canning CG, Lee MJ. Inter-limb coordination in bimanual reach-to-grasp following stroke. Disability and Rehabilitation. 2009:1435.

## Slide 32: Methodology
Statistical Analysis:
  Linear mixed model using between-subject factors and within-subject factors
  Separate two-way repeated measures ANOVAs to analyze primary motor cortex activity and motor task performance.
    [2 x 3; hand (non-preferred versus preferred) x group (amputee, simulator, and control)]
  One-way ANOVAs were used to examine motor performance for individual hands, as well as movement asynchrony and brain laterality index
  Independent t-tests were performed for the detection of significance in the survey measures
  A p-value of ≤ 0.05 was considered statistically significant for all comparisons

## Slide 33: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 34: Results: Movement Synchrony
Hypothesis 1a. Bimanual coordination will be significantly higher in the control group than prosthesis and simulator groups.
  Movement asynchrony was not significantly different when comparing the control group to the TD-Simulator and ULD groups for any component of task motion
    General trends of coordination showed ULD participants had overall higher movement asynchrony
Overall Task Time |  | 
 | Preferred Hand | Non-Preferred Hand
Prosthesis | 9.442 ± 3.688s | 10.828 ± 5.013s
Prosthesis Simulator | 6.061 ± 2.657s | 6.421 ± 2.778s
Control | 2.102 ± 1.179s | 2.216 ± 1.306s

## Slide 35: Results: Movement Synchrony
Hypothesis 1a. Bimanual coordination will be significantly higher in the control group than prosthesis and simulator groups.
  ULD subjects adopted a preferred limb dominated task strategy
  TD-Control subjects had closer mean asynchrony values to zero
  TD-Simulator subjects tended to lead task motion with the non-preferred limb
Overall Task Time |  | 
 | Preferred Hand | Non-Preferred Hand
Prosthesis | 9.442 ± 3.688s | 10.828 ± 5.013s
Prosthesis Simulator | 6.061 ± 2.657s | 6.421 ± 2.778s
Control | 2.102 ± 1.179s | 2.216 ± 1.306s

## Slide 36: Results: Movement Synchrony
Hypothesis 1a. Bimanual coordination will be significantly higher in the control group than prosthesis and simulator groups.
  Assessing motor function using overall movement time shows:
    ULD group takes significantly longer (p = 0.007) than both the TD-Control and TD-Simulator conditions
    TD-Simulator subjects took significantly longer (p = 0.007) than TD-Control subjects
Overall Task Time |  | 
 | Preferred Hand | Non-Preferred Hand
Prosthesis | 9.442 ± 3.688s | 10.828 ± 5.013s
Prosthesis Simulator | 6.061 ± 2.657s | 6.421 ± 2.778s
Control | 2.102 ± 1.179s | 2.216 ± 1.306s
Chart: Bimanual Coordination
| Hand-to-Tray | Tray Transfer | Hand Return | Overall
ULD | 2.3489 | 1.9099 | 5.47 | 10.8275
Non-Affected | 1.0284 | 0.98893 | 2.1879 | 6.061
TD-Simulator | 1.3951 | 1.4351 | 1.9989 | 6.4214
TD-Control | 0.58127 | 0.5522 | 0.76127 | 2.2157
Dominant | 0.54993 | 0.46767 | 0.65793 | 2.1019
ULD2 | 2.2222 | 2.3936 | 4.0451 | 9.4427

## Slide 37: Results: Gross Manual Dexterity
Hypothesis 1b. Gross manual dexterity will be significantly higher in the control group than prosthesis and simulator groups.
  Significant main effects were found for both limb condition (F(2,3) = 34.864, p = 0.008) and hand (F(1,4) = 63.043, p < 0.001)
  Box and Block task performance was significantly lower (p = 0.008) in both TD-Simulator and ULD subjects compared to TD-Control participants
  ULD and TD-Simulator subjects performed with no significant differences (p = 0.948) for the non-preferred limb
Task Performance (Blocks Transferred) |  | 
 | Preferred Hand | Non-Preferred Hand
Prosthesis | 37.40 ± 6.65 | 7.23 ± 3.37
Prosthesis Simulator | 47.60 ± 17.31 | 7.63 ± 5.61
Control | 47.60 ± 17.31 | 49.43 ± 15.21

## Slide 38: Results: Brain Activation
Hypothesis 2a. Brain Activity in the motor cortex will be significantly increased, possibly due to exploratory movements, for both prosthetic and simulator conditions compared to the control group.
  No significant main effects for hand (F(1,4) = 7.509, p = 0.052) and limb (F(2,3) = 0.570, p = 0.617) conditions
  No interaction effect (F(2,3) = 1.092, p = 0.440)
Chart: Left.........................Region of Interest......................Right
TD-Control - Preferred Hand | 0.04567 | 0.01651 | 0.073293 | 0.13076 | 0.15298 | 0.15087 | 0.06093 | 0.05371
ULD - Preferred Hand | 0.37019 | 0.24546 | 0.2418 | 0.12507 | 0.19626 | 0.22718 | 0.16883 | 0.16176 | 0.38567
Chart: Left.........................Region of Interest......................Right
TD-Control - Non-Preferred Hand | 0.32285 | 0.14255 | 0.059329 | 0.22395 | 0.3839 | 0.058002 | 0.36437 | 0.19073 | 0.18343 | 0.19983
TD-Simulator Non-Preferred Hand | 0.096926 | 0.17321 | 0.13096 | 0.15676 | 0.321 | 0.051806 | 0.4526 | 0.29035 | 0.37389 | 0.13028
ULD - Non-Preferred Hand | 0.22321 | 0.21523 | 0.048608 | 0.40296 | 0.081485 | 0.11188 | 0.34773 | 0.7168 | 0.03469

## Slide 39: Results: Brain Activation
Hypothesis 2a. Brain Activity in the motor cortex will be significantly increased, possibly due to exploratory movements, for both prosthetic and simulator conditions compared to the control group.
  Independent t-test on the two hand conditions yielded significant differences between preferred (M = 0.0852 µmol, SD = 0.1525 µmol) and non-preferred (M = 0.2926 µmol, SD = 0.2856 µmol) hands; t(28) = -2.480, p = 0.019
Chart: Left.........................Region of Interest......................Right
TD-Control - Preferred Hand | 0.04567 | 0.01651 | 0.073293 | 0.13076 | 0.15298 | 0.15087 | 0.06093 | 0.05371
ULD - Preferred Hand | 0.37019 | 0.24546 | 0.2418 | 0.12507 | 0.19626 | 0.22718 | 0.16883 | 0.16176 | 0.38567
Chart: Left.........................Region of Interest......................Right
TD-Control - Non-Preferred Hand | 0.32285 | 0.14255 | 0.059329 | 0.22395 | 0.3839 | 0.058002 | 0.36437 | 0.19073 | 0.18343 | 0.19983
TD-Simulator Non-Preferred Hand | 0.096926 | 0.17321 | 0.13096 | 0.15676 | 0.321 | 0.051806 | 0.4526 | 0.29035 | 0.37389 | 0.13028
ULD - Non-Preferred Hand | 0.22321 | 0.21523 | 0.048608 | 0.40296 | 0.081485 | 0.11188 | 0.34773 | 0.7168 | 0.03469

## Slide 40: Results: Laterality Index
Hypothesis 2b. Brain Activity in the motor cortex will be less lateralized for both prosthetic and simulator conditions compared to the control group.
  No effects were statistically significant at the 0.05 significance level
    Main effect for hand (F(1,4) = 0.136, p = 0.731) demonstrated no significant difference between preferred (M = -0.113, SD = 0.152) and non-preferred (M = -0.178, SD = 0.077) hands
    Main effect for limb condition (F(2,3) = 0.212, p = 0.820) showed no significant difference between ULD (M = -0.091, SD = 0.105), TD-Simulator (M = -0.153, SD = 0.191) and TD-Control (M = -0.193, SD = 0.141) groups
    The interaction effect was not significant, F(2,3) = 0.505, p = 0.647
  One-way analyses of variance also showed no significance when collapsed along each set of conditions

## Slide 41: Results: Laterality Index
Hypothesis 2b. Brain Activity in the motor cortex will be less lateralized for both prosthetic and simulator conditions compared to the control group.
  Means and standard deviations may indicate less lateralization in the ULD population than in the TD conditions
  This would support the hypothesis, but is not statistically significant
Chart: Preferred Hand Non-Preferred Hand
| Preferred | Non-Preferred
 | -0.113 | -0.178
Chart: ULD TD-Simulator TD-Control
| ULD | TD-Simulator | TD-Control
 | -0.091 | -0.153 | -0.193

## Slide 42: Results: Body Perception
Hypothesis 3. Embodiment and agency of the non-preferred arm will be significantly higher in the control group compared to prosthesis users.
  For both the ESSS and BFQ, there were no significant differences in scoring between TD and ULD participants
  Many expected subscales show mean differences between the two groups
    Narrative, Agency and “Right” show large mean differences
 | ESSS |  |  | BFQ | 
 | Narrative | Agency | Embodiment | Arms Scale | "Right" Scale
ULD | 14.40 ± 5.50 | 15.20 ±5.85 | 15.40 ± 6.84 | 10.00 ± 1.41 | 13.00 ± 2.83
TD | 20.67 ± 8.14 | 23.33 ± 10.06 | 17.00 ± 7.55 | 11.00 ± 5.29 | 9.33 ± 5.13

## Slide 43: Results: Body Perception
 | ESSS |  |  | BFQ | 
 | Narrative | Agency | Embodiment | Arms Scale | "Right" Scale
ULD | 14.40 ± 5.50 | 15.20 ±5.85 | 15.40 ± 6.84 | 10.00 ± 1.41 | 13.00 ± 2.83
TD | 20.67 ± 8.14 | 23.33 ± 10.06 | 17.00 ± 7.55 | 11.00 ± 5.29 | 9.33 ± 5.13

## Slide 44: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 45: Discussion: Movement Synchrony
Potential coordination deficits observed in bimanual reaching could indicate reduced function earlier in life than has been previously assumed
Differences in movement strategy could point to underlying neurological differences in the treatment of the prosthetic devices
  Tool use vs. Embodiment
  Differences in specificity of neural selection leading to altered hand dominance
  Slower movements due to underdeveloped motor repertoires and exploratory movements
It is anticipated that movement strategies in the ULD group may follow similar trends to control subjects with earlier prosthesis prescription due to enhanced neuronal group selection

## Slide 46: Discussion: Movement Synchrony
Slower ULD performance of bimanual task may be caused by:
  Use of a novel prosthetic device
    Not the only factor, due to significantly faster performance of simulator users
  Differences in motor control strategies
    ULD subjects may have used less efficient exploratory motions
In order to better assess the accuracy of this assessment, future studies would benefit from longitudinal testing of motor performance in all groups

## Slide 47: Discussion: Prosthetic Simulators
Lack of significant differences between simulator and prosthesis users during Box and Block task could indicate that prosthetic simulators are effective surrogates for amputees
  Can potentially improve statistical power and enhance iterative device design
Statistically significant (p = 0.007) differences in bimanual tasks potentially caused by:
  Differences in motor repertoires
  Muscle weakness/fatigue
Future direction: Inclusion of wrist flexor/extensor strength measurements as potential factor in motor performance differences

## Slide 48: Discussion: Brain Activation/Laterality
Despite a lack of significance, some expected trends were observed:
  Higher mean activation in prosthesis and simulator users
  Lower lateralization in ULD and TD-Simulator subjects
These trends are potentially caused by:
  Increased ipsilateral activation in the performance of cognitively demanding tasks
  Less experience and learning with the non-preferred limb
The collection of more data to test for statistical significance should be warranted

## Slide 49: Discussion: Body Perception
Lack of statistical significance is likely a result of sample size
  60% response rate yielded only three responses for each survey
Some anticipated trends appear to be present in ULD subjects:
  Decreased embodiment
  Decreased agency
  Reduced affected limb prominence
With more responses from both ULD and TD subjects, it is expected that these trends would persist and become statistically significant

## Slide 50: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 51: Limitations
Equipment Limitations:
  fNIRS:
    Movement artifacts during testing could lead to erroneous HBO and HBR readings
    Dark hair can prevent probe function
    Probe placement varies based on head size
      Placement is approximated based on standards, due to lack of co-registered brain image (MRI)
    Low temporal accuracy
  Bimanual Coordination Tray:
    Some movement timing may not be captured by integrated sensors
      Synchronous camera footage can be used to find timing in these cases
    The tray cannot be scaled for different subject dimensions (arm length, shoulder width, etc.)

## Slide 52: Possible Limitations
Experiment Limitations:
  Subject Pool:
    Subject pool for ULDs is small, and many have used prostheses before
      Limited number of subjects restricts study population size
      Prior prosthesis users are accounted for with minimum 6 month abandonment of prior prosthetic
    Pediatric population limits the number of feasible fNIRS trials
    Movement artifacts are common while testing children
      Any erroneous movements will be documented and filtered from data
    Typically developing children are matched for age and sex
    Handedness is controversial for ULD subjects
    Large range of subject ages and levels of amputation

## Slide 53: Agenda
Introduction/Background
Statement of the Problem
Theoretical Framework
Overview of Existing Literature
Methodology
Results
Discussion
Limitations
Conclusion

## Slide 54: Conclusion
Systemic deficits are present in both unimanual and bimanual motor tasks
  In the performance of unimanual activities, a prosthesis simulator behaves nearly identically to an actual prosthesis user
    Prosthesis simulators show promise as substitutes for ULD subjects
  Performance differences with bimanual activities show that learning effects from novel device use are not the only factor in reduced performance
  Prosthesis use may help to improve these motor deficits
There are no significant differences present in brain activity, brain lateralization, and perceived embodiment, agency and body image
  Despite a lack of significant differences in brain activity, lateralization and body perception, many potential trends are visible in the data which warrant further exploration
Future research should explore, with a larger subject pool, fNIRS and survey measures used in this study to search for possible significance

## Slide 55: Acknowledgements
People
  Jorge Zuniga, PhD
  Mukul Mukherjee, PhD
  Ka-Chun Siu, PhD
  Drew Dudley
  David Salazar
  Keaton Young
  Walker Arce
  Claudia Cortes-Reyes
  Chris Copeland
  Nick Than
Funding:
  NASA Nebraska Space Grant Fellowship
  Graduate Research and Creative Activity (GRACA) Grant

## Slide 56
Questions/Suggestions?

## Slide 57: References
Krebs D, Edelstein J, Thornby M. Prosthetic management of children with limb deficiencies. Physical Therapy. 1991;71(12):920.
Hadders-Algra M. The neuronal group selection theory: A framework to explain variation in normal motor development. Dev Med Child Neurol. 2000;42(8):566-572. doi: 10.1017/S0012162200001067.
Hadders-Algra M M. The neuronal group selection theory: Promising principles for understanding and treating developmental motor disorders. Dev Med Child Neurol. 2000-10;42(10):707-15.
Facts about upper and lower limb reduction defects. . 2016.
About ABS - amniotic constriction band syndrome. (n.d.).
James MA, Bagley AM, Brasington K, Lutz C, McConnell S, Molitor F. Impact of prostheses on function and quality of life for children with unilateral congenital below-the-elbow deficiency. J Bone Joint Surg Am. 2006;88(11):2356-2365.
Meurs M, Maathuis CG, Lucas C, Hadders-Algra M, van der Sluis CK. Prescription of the first prosthesis and later use in children with congenital unilateral upper limb deficiency: A systematic review. Prosthetics and Orthotics International. 2006;30(2):165-173.
Huizing K, Reinders-Messelink H, Maathuis C, Hadders-Algra M, van der Sluis CK. Age at first prosthetic fitting and later functional outcome in children and young adults with unilateral congenital below-elbow deficiency: A cross-sectional study. Prosthetics and orthotics international. 2010;34(2):166-174.
Zuniga JM, Pierce III JE, Than N, et al. Function of a 3D printed transitional prosthesis. . 2017.
Do EY, Hsiao C, Zhao C. The digital box and block test automating traditional post-stroke rehabilitation assessment. PerCom Workshop. 2013.
Korkmaz M, Erbahceci F, Ulger O. Evaluation of functionality in acquired and congenital upper extremity child amputees. Acta Orthop Traumatol Turc. 2012;46:262-268.

## Slide 58: References
Dromerick A, Schabowsky C, Holley R, Monroe B, Markotic A, Lum P. Effect of training on upper-extremity prosthetic performance and motor learning: A single-case study. Arch Phys Med Rehabil. 2008;89:1199.
Tihanyi J. Body schema and body awareness of amputees. . Prosthetics and Orthotics International. 2008;32:363-382.
Imaizumi S, Asai T, Koyama S. Embodied prosthetic arm stabilizes body posture, while unembodied one perturbs it. Consciousness and Cognition. 2016;45(Supplement C):75-88. doi: https://doi.org/10.1016/j.concog.2016.08.019.
Sporns O, Edelman GM. Solving bernstein's problem: A proposal for the development of coordinated movement by selection. Child Development. 1993;64:960-981.
Polovina S, Škorić Polovina T, Polovina A, Polovina-Prološčić T. Intensive rehabilitation in children with cerebral palsy: Our view on the neuronal group selection theory. Collegium antropologicum. 2010;34(3):981-988.
Valk TA, Mouton LJ, Bongers RM. Joint-angle coordination patterns ensure stabilization of a body-plus-tool system in point-to-point movements with a rod. Frontiers in psychology. 2016;7:826.
Huinink LHB, Bouwsema H, Plettenburg DH, van der Sluis CK, Bongers RM. Learning to use a body-powered prosthesis: Changes in functionality and kinematics. Journal of NeuroEngineering and Rehabilitation. 2016;13(1):90. https://doi.org/10.1186/s12984-016-0197-7. Accessed 9/12/2017 1:16:10 PM.
Weeks DL, Wallace SA, Anderson DI. Training with an upper-limb prosthetic simulator to enhance transfer of skill across limbs. Arch Phys Med Rehabil. 2003;84. https://doi.org/10.1053/apmr.2003.50014. Accessed 9/12/2017 1:16:10 PM.
Weeks DL, Anderson DI, Wallace SA. The role of variability in practice structure when learning to use an upper-extremity prosthesis. J Prosthet Orthot. 2003;15. https://doi.org/10.1097/00008526-200307000-00006. Accessed 9/12/2017 1:16:10 PM.
Field-Fote EC, Tepavac D. Improved intralimb coordination in people with incomplete spinal cord injury following training with body weight support and electrical stimulation. Physical Therapy. 2002;82(7):707-715.
Huinink LHB, Bouwsema H, Plettenburg DH, van dS, Bongers RM. Learning to use a body-powered prosthesis: Changes in functionality and kinematics. Journal of NeuroEngineering and Rehabilitation. 2016;13(1):90. https://doi.org/10.1186/s12984-016-0197-7. doi: 10.1186/s12984-016-0197-7.

## Slide 59: References
Kilbreath SL, Crosbie J, Canning CG, Lee MJ. Inter-limb coordination in bimanual reach-to-grasp following stroke. Disability and Rehabilitation. 2009:1435.
Nishiyori R, Bisconti S, Ulrich B. Motor cortex activity during functional motor skills: An fNIRS study. Brain topography. 2016;29(1):42-55.
Semjen A. Bimanual coordination during rhythmic movements in the absence of somatosensory feedback. . 2005;94.
Tian F, Delgado MR, Dhamne SC, et al. Quantification of functional near infrared spectroscopy to assess cortical reorganization in children with cerebral palsy. Opt.Express. 2010;18(25):25973-25986. http://www.opticsexpress.org/abstract.cfm?URI=oe-18-25-25973. doi: 10.1364/OE.18.025973.
Giele H, Giele C, Bower C, Allison M. The incidence and epidemiology of congenital upper limb anomalies: A total population study. The journal of hand surgery. 2001;26(4):628-634.
Canfield MA, Honein MA, Yuskiv N. National estimates and race/ethnic-specific variation of selected birth defects in the united states, 1999-2001. Birth defects research. Part A, Clinical and molecular teratology. 2006;76(11):747-756.
Resnik L, Meucci MR, Lieberman-Klinger S. Advanced upper limb prosthetic devices: Implications for upper limb prosthetic rehabilitation. Arch Phys Med Rehabil. 2012;93(4):710-717.
Resnik L. Development and testing of new upper-limb prosthetic devices: Research designs for usability testing. Journal of rehabilitation research and development. 2011;48(6):697-706.
Hadders-Algra M, Reinders-Messelink HA, Huizing K, van den Berg R, van der Sluis CK, Maathuis CGB. Use and functioning of the affected limb in children with unilateral congenital below-elbow deficiency during infancy and preschool age: A longitudinal observational multiple case study. Early Human Development. 2013;89(1):49-54. doi: https://doi.org/10.1016/j.earlhumdev.2012.07.011.
Biddiss EA, Chau TT. Upper limb prosthesis use and abandonment: A survey of the last 25 years. Prosthet Orthot Int. 2007;31. https://doi.org/10.1080/03093640600994581. Accessed 9/12/2017 1:16:10 PM.
Zuniga JM, Carson AM, Peck JM, Kalina T, Srivastava RM, Peck K. The development of a low-cost three-dimensional printed shoulder, arm, and hand prostheses for children. Prosthetics and Orthotics International. 2016.

## Slide 60: References
Zuniga JM, Katsavelis D, Peck JM. Cyborg beast: A low-cost 3d-printed prosthetic hand for children with upper-limb differences. BMC research notes. 2015;8(1):10.
Zuniga JM, Peck J, Srivastava R, Katsavelis D, Carson A. An open source 3D-printed transitional hand prosthesis for children. JPO: Journal of Prosthetics and Orthotics. 2016;28(3):103-108.
Rajak BL, Gupta M, Bhatia D. Growth and advancements in neural control of limb. Biomedical Science and Engineering. 2015;3(3):46-64.
Nishiyori R. fNIRS: An emergent method to document functional cortical activity during infant movements. Frontiers in psychology. 2016;7:533.
Mathiowetz V, Wiemer D, Federman S. Grip and pinch strength: Norms for 6- to 19-year-olds. The American journal of occupational therapy. 1986;40(10):705-711.
Petersson C, Simeonsson RJ, Enskar K, Huus K. Comparing children's self-report instruments for health-related quality of life using the international classification of functioning, disability and health for children and youth (ICF- CY). Health and quality of life outcomes. 2013;11(75).
Reilly KT, Sirigu A. Motor cortex representation of the upper-limb in individuals born without a hand. PLoS One. 2011;6(4).
Shirota C, Jansa J, Diaz J, et al. On the assessment of coordination between upper extremities: Towards a common language between rehabilitation engineers, clinicians and neuroscientists. Journal of NeuroEngineering and Rehabilitation. 2016;13(1):80.
Burgess Limerick R, Abernethy B, Neal RJ. Relative phase quantifies interjoint coordination. Journal of biomechanics. 1993;26(1):91-94.
Franz EA, Rowse A, Ballantine B. Does handedness determine which hand leads in a bimanual task? Journal of Motor Behavior. 2002;34(4):402-412.

## Slide 61: Review of Literature
Huizing et al. (2010):
  Participants:
    Twenty subjects aged 6 – 21 years
      5 prosthesis users and 15 non-users
  Methods:
    Administered two general surveys
    Given a standardized prosthesis functionality task set
    Performed video analysis of common activities of daily life

## Slide 62: Review of Literature
Huizing et al. (2010):
  Results:
    Early prosthesis adoption (< 1 year of age) significantly increased duration of prosthesis usage and overall satisfaction with prosthesis usefulness (p < 0.05)
    No significant effect on gross motor function outside of specialized tasks
  Conclusion: Trade-offs must be considered when adopting a prosthesis
    Having an analogue for an intact arm does enrich the patients potential motor repertoires
    There is an inherent reduction in sensory repertoires introduced by the prosthesis’ socket attachment

## Slide 63: Review of Literature
Meurs et al. (2006):
  Children fitted with a prosthesis earlier in life (< 2 years of age) were both happier and rejected their device less often (pooled Odds Ratio = 3.6, 95% CI)
  Because few functional benefits were apparent, it was suggested that the decision for device fitting be left to the discretion of the clinician and the family of the patient

## Slide 64: Review of Literature
Korkmaz et al. (2011):
  Participants:
    40 children aged 8 – 17 years (n = 20 acquired and n = 20 congenital)
  Methods:
    CAPP-FSI and PUFI were administered at fitting, after three weeks and after six months of use
  Results:
    Significant improvements for both the acquired and congenital groups
    Overall upper limb functionality improved as a result of the intervention at both three weeks and six months
    Tactile sensation, coordinated motions of the hand, and proprioceptive feedback were partially improved by the prosthesis

## Slide 65: Review of Literature
Zuniga et al. (2017):
  Participants:
    Eleven children (n = 5 female) aged three to fifteen years
  Methods:
    Box and Block gross manual dexterity test
    Tested at fitting with a 1-6 month retest
  Results:
    Retest gross dexterity (13.0 ± 12.7 blocks per minute) was significantly improved over baseline (6.3 ± 12.3 blocks per minute)
      Indicates promise for the development of further motor skills and improvements in quality of life

## Slide 66: Review of Literature
Reilly & Sirigu (2011):
  Participants:
    Four females with congenital ULDs (aged 25 to 38 years)
    2 agenesis, 2 in utero amputations
  Methods:
    Transcranial Magnetic Stimulation (TMS) was used to evoke motor potentials in the hand areas of the primary motor cortex (M1)
  Results:
    TMS never induced the sensation that the missing limb was present
    No sensations of movement in the missing limb were felt
  Conclusion:
    There was no readily activated neural representation for the missing limb
    There may be a significant difference in the homunculus between typically developing individuals and those with ULDs

## Slide 67: Review of Literature
Hadders-Algra et al. (2000):
  Application of NGST to developmental abnormalities in cerebral palsy (CP) and developmental coordination disorder (DCD)
  Underlying cause of functional deficits is likely due to dysfunction in neuronal groups associated with the primary motor repertoires for these actions
  The author recommends reduction of sensorimotor dyscoordination as a potential rehabilitation

## Slide 68: Review of Literature
Polovina et al. (2010):
  Participants:
    24 children aged 12 to 55 months (mean = 19.5) with CP
  Methods:
    Rehabilitation using intensive and variable sensorimotor stimuli as well as the passive facilitation of normal movement patterns for at least three hours per day
  Results:
    All dysfunction severity levels saw significant improvements in function
    Many children needed reclassification into less severe classifications
  Conclusion:
    The reason for this difference is the controlling of sensorimotor inputs and encouragement of healthy motion in early development, which leads to more healthy neuronal group selection over the course of time

## Slide 69: Review of Literature
Tihanyi et al. (2008):
  Participants:
    51 individuals with varied amputations
  Methods:
    Questionnaires for body schema and body awareness were administered
  Results:
    Prosthesis usage significantly improved:
      Proprioception-based accuracy in both upper- and lower-limb amputees
      Elongation of sensed phantom limb movement to match prosthesis length
      Weight distribution during passive standing
      Ownership of the affected limb

## Slide 70: Review of Literature
Imaizumi et al. (2016):
  Participants:
    Nine subjects with ULDs
  Methods:
    Assessment of postural sway using a WiiFit Balance Board (Nintendo Co., Ltd., Kyoto, Japan) both with and without prosthesis
  Results:
    Users with a greater level of body schema incorporation over their prostheses had less postural sway while wearing the prosthesis
    Non-users experienced more sway while wearing the prosthesis
  Conclusion:
    Prostheses can be used effectively as an analogue for an intact arm in developing postural control and coordination mechanisms if embodied

## Slide 71: Review of Literature
Nishiyori et al. (2016):
  Participants:
    12 healthy, right-handed adults (mean age = 23.41±5.1 -years, 8 females)
  Methods:
    Performance of stepping in place and unimanual/bimanual reaching while being monitored by fNIRS
  Results:
    Significantly higher activation (HBO) in the brain hemisphere contralateral to the limb used in the performed task
    Higher activation in both hemispheres during the performance of bimanual reaching activities
    Reaching had consistently more lateral activation patterns than stepping

## Slide 72: Review of Literature
Tian et al. (2010):
  Participants:
    Children aged 6-16 years with and without CP
  Methods:
    Repeated four-finger tapping tasks using fNIRS
  Results:
    Control subjects had contalateral laterality indices to that of the task limb
    CP subjects had mixed contralateral and ipsilateral hemodynamic responses
    As age increased, LI increased
      Enhanced specialization for involved neuronal groups

## Slide 73: Review of Literature
Kilbreath et al. (2006):
  Participants:
    13 stroke victims aged 55-77 years
  Methods:
    “Novel” unimanual and bimanual reaching tasks with sensorized tray
  Results:
    Stroke victims took significantly longer to complete the task
    No significant differences between stroke victims and controls in terms of movement synchrony

## Slide 74: Review of Literature
Semjen et al. (2005):
  Participants:
    2 deafferented subjects (one unilateral and one bilateral)
    3 healthy control subjects
  Methods:
    Two-dimensional circle drawing task
      Both hands visible, one hand visible, and no hands visible
      Comfortable speed and “as fast as possible”
  Results:
    Significant trajectory degradation associated with restricted vision, increased speed, and opposing directions
      Present in all groups, but more severe in deafferented subjects
    Coordination was severely impacted by deafferentation

## Slide 75: Review of Literature
Franz et al. (2002):
  Participants:
    Right (n = 16) and left (n = 16) handed subjects
  Methods:
    Circles were traced using the index finger in both symmetrical and opposing directions
  Results:
    Negligible difference in temporal coordination for both groups when the circles were traced in the same direction
    Significant latency for opposing tracing task

## Slide 76: Review of Literature
Weeks et al. (2003):
  Participants:
    42 right-handed adults (21 men: mean age, 22.4y; 21 women: mean age, 22.7y)
  Methods:
    Three conditions: dominant hand prosthesis simulator practice, non-dominant hand prosthesis simulator practice, and control
    Three randomized functional tasks were performed: toggling a switch, placing a dowel in a hole, and prehension/placement of a large peg
    Assessed during practice, pre-test and 24 hour post-test
  Results:
    Initiation time was found to improve significantly at post-test (p = 0.003) and retest (p = 0.029)
      Simulator dominance had no significant effects
    Movement time was also significantly lower for both practice groups than the control group (p = 0.026)

## Slide 77: Review of Literature
Huizink et al. (2016):
  Participants:
    30 right-handed, able-bodied participants (14 males, 16 females; age 21.37 ± 1.81 years)
    17 controls (7 males, 10 females; age 23.29 ± 1.45 years)
  Methods:
    Performing grasping tasks with spring-loaded, deformable objects of variable compressibility using a prosthetic simulator
    Five training sessions over the course of two weeks
    Function was assessed using the Southampton Hand Assessment Procedure (SHAP)
  Results:
    Significant decrease in movement time required to complete tasks (p < 0.001)
    Significant decrease in hook closing time (p < 0.01)